Sample Painted Pavement Marking Bid Documents

Bid documents are critical for most county road projects. Half of the NIRMA member counties either have no bid specifications, documents, etc. or have substandard bid documents meaning they are lacking important requirements such as proper material and application specifications, traffic control, liability insurance requirements, etc.

Not requiring proper specifications and other important required information allows contractors to provide substandard projects and opens the county to liability that could easily be avoided with the proper bid documents.

Dollar thresholds under The County Purchasing Act, most recently revised in 2018, are as follows:

- $50,000 or more (previously $20,000 or more) - Competitive sealed bidding process is required;

(b) $10,000 or greater and less than $50,000 (previously $5,000 or greater and less than

$20,000) - By securing and recording at least three informal bids, if practicable; or

(c) Less than $10,000 (previously less than $5,000) - By purchasing in the open market if

the estimated value of the purchase is less than $10,000, subject to section 23-3112.

In any county having a population of less than 100,000 inhabitants and in which the

county board has not appointed a purchasing agent pursuant to section 23-3105, all

elected officials are hereby authorized to make purchases with an estimated value less

than $10,000. Section 23-3108(1).

Even if your painted pavement marking project cost does not meet the $50,000 required bid limit, three informal written quotes/bids are required under the above County Purchasing Act. The following information can be used for your informal bids/quotes as well as for a project costing less than $10,000, where no quotes are required.

No matter the cost of the project, counties still should require the proper materials and application specifications, traffic control, and liability insurance to ensure a satisfactory project and to protect the motoring public’s safety and the county from liability.

The following sample Painted Pavement Marking bid document was developed in WORD form for easy alterations to fit each county’s specific need. Sample paint material and application specifications are included in red.

A sample bid can be used with county supplying paint and glass beads, purchased off state bid, and contractor application only OR the contractor supplying paint, glass beads, and application can be specified. Simple alterations need to be made. Application rates can be easily altered to fit your specific project requirements.

Sample bid advertisement public notice and “Notice to Proceed” documents are also included for your use. Just fill in the appropriate dates.

Please let me know of any questions by calling 402-310-4417 or email tim@nirma.info.

Tim Baxter

NIRMA Road Safety and Loss Prevention Specialist

BID DOCUMENTS AND SPECIFICATIONS

FOR

# ___________________ COUNTY ROAD DEPARTMENT

PAINTED PAVEMENT MARKING PROJECT _______________

____________ COUNTY, NEBRASKA

Bid Opening ____ a.m.

Month/Day/Year

_______________________ COUNTY ROAD DEPARTMENT

PAINTED PAVEMENT MARKING

Sealed Bids, clearly marked "PAINTED PAVEMENT MARKING BID" will be received at the office of the _______________________ County Clerk, _______________________ County Courthouse, ___________,  Nebraska XXXXX, until ____ A.M. on __________, 20___, for approximately ____ miles of painted pavement marking.  Bids will be publicly opened and read at that time in the _______________________ County Board of Commissioners/Supervisors room during their regularly scheduled meeting.

PAINTED PAVEMENT MARKING SPECIFICATIONS

A. MATERIALS – 	County will supply traffic paint and glass beads. (OR) Contractor will supply traffic paint and glass beads. Must be determined prior to bid advertisement. If bid requires Contractor to purchase paint and glass beads, County will provide a Tax Exemption Certificate as applicable.

1. Paint

The contractor shall use a traffic paint that can be applied under the temperature conditions existing at the time of application. Traffic paint shall be Acrylic Resin Lead and Chromium Free Waterborne Traffic Paint.

The paint shall be furnished ready mixed and shall not be diluted or thinned. When applied at a wet film minimum thickness of    18     mils the paint shall provide a    five-inch    wide stripe that dries within the specified time. The traffic paint shall be compatible with drop-on glass beads, providing good adhesion and good refraction. The colors for the white paint used for edge line and the yellow paint used for centerline shall meet State of Nebraska Department of Transportation traffic paint color specifications.

The traffic paints will be accepted on the basis of a Manufacturer’s Certified Test Results indicating that the paint meets the requirements of the current Nebraska Department of Transportation Specification for Traffic Paint.

2. Glass Beads

Glass beads for use with Acrylic Waterborne Traffic Paint shall be designated as AASHTO M247, Type I, drop-on, dual-coated moisture resistant and shall meet the latest Nebraska Department of Transportation’s Specification Requirements. Glass beads shall be applied at a rate of ___8___ lbs. per gallon of paint.

B. CONSTRUCTION REQUIREMENTS

1. Equipment

Longitudinal paint marking lines shall be applied with a self-propelled, riding-type line striper capable of applying solid or continuous lines and broken or skip lines at regular intervals, and capable of mechanically applying a regulated amount of glass beads directly to the wet film surface of the marking paint. The glass bead nozzles or guns shall be mounted directly behind the paint guns.

Paint marking symbols shall be applied with equipment and application designed for the appropriate type of pavement marking material.

2. Pavement Preparation

The surface on which paint is to be applied shall be clean and dry. Paint shall not be applied in damp conditions or if there is any evidence of surface moisture on the pavement

3. Weather Limitations

Paint markings shall not be installed at pavement, air, or paint temperature less than 50° F. Waterborne paint may be heated to a maximum of 150° F. Manufacturer’s weather limitations shall be followed.

4. Hours of Work

All work shall be conducted during daylight hours only. Any requests for working hours not included in the given time frame must be submitted in writing to the Highway Superintendent for approval.

C. PAINT APPLICATION

1. Paint shall be machine applied using spray guns designed and adjusted to apply paint at the required thickness and width. If there is any evidence of gun clogging, splattering, or uneven paint distribution, painting operations shall cease until equipment is restored to proper operation.

2. Painting of stop lines, arrows, words, and symbols may be applied by hand using paint spray equipment, stencils, templates, and guides as necessary. Equipment shall be capable of applying paint evenly to the required thickness. Dimensions shall meet the most recent adopted edition of the Manual on Uniform Traffic Control Devices.

3. Provide the Highway Superintendent with a copy of the manufacturer’s paint and glass bead specifications and application instructions if contractor supplies paint.

4. Paint will be applied at a minimum of   18   mil thickness wet or estimated 12 gallons per mile on centerline/no passing and estimated 42 gallons per mile on both edgelines. Center and edge lines shall be   5” in width. Painted Pavement Markings shall be performed in accordance with the most recent adopted edition of the Manual on Uniform Traffic Control Devices and the State of Nebraska Specifications for Painted Pavement Markings.

5. Paint will be applied to match existing center skip lines, no passing lines, and edge lines. Should project have no discernable striping, county will mark no passing zones. Centerline skip paint will be applied consisting of a ten foot line with a thirty-foot skip pattern.

D. DROP-ON GLASS BEAD APPLICATION

1. Drop-on glass beads shall be mechanically applied to the wet paint directly behind the paint spray guns. Glass bead dispenser shall be equipped with an automatic cut-off control synchronized with the cut-off of the paint. Glass beads shall be applied at a rate of   8   pounds of glass beads for each gallon of paint. For stop lines, arrows, words, and symbols, glass beads may be applied by hand. Glass beads shall be applied evenly and shall completely cover the painted area. If beads do not embed properly in the paint, all marking operations shall cease until corrections are made.

2. Beads shall be applied so that they receive maximum capture and binding by the paint to produce a highly reflective, weather, and wear resistant traffic line.

E. QUALITY OF WORK

1. Apply pavement markings straight and close to the intended alignment without abrupt changes that result in an unacceptable appearance. Lines that deviate laterally from the intended alignment more than 2 inches in 200 feet may be rejected.

2. Remove and replace pavement markings that have:

• drag marks			• improper adhesion

• gashes			• improper width, length, or thickness

• gouges			• areas that have failed to solidify

• foreign covering		• areas that present a ragged appearance

• discolored areas		• areas that do not present sharply defined edges

• areas with abrupt, unintended changes in alignment

3. Removal/replacement of unsatisfactory pavement marking will be at Contractor’s expense.

F. TIME OF COMPLETION

1. Painted Pavement Markings will be applied and completed by no later than ________, 20___.

G. MEASUREMENT AND PAYMENT

1. Pavement markings installed in conformance with the Detailed Specifications and acceptable to the Highway Superintendent shall be measured as actual material applied to the pavement and paid for at the contract unit price bid per mile.

2. Such payment shall be full compensation for preparation of pavement surface, removing and disposing of all existing material, furnishing (unless furnished by county) and installing marking materials, and for all labor, equipment, tools materials, traffic control, and incidentals necessary to complete the Work.

3. All materials (unless furnished by county), equipment, labor, and incidentals necessary to complete the work that is not paid for directly, shall be considered subsidiary to items for which payment is made.

4. Any increase or decrease of project length will be at the discretion of the Highway Superintendent. Additional pavement paint marking will be performed at bid price.

5. Payment will be made to contractor within 45 days of satisfactory completion and acceptance of project.

H. QUANTITIES

1. The County reserves the right to change the quantities, delete sections, or add sections, and no adjustment in unit price will be made for any change in any quantity.

I. TRAFFIC CONTROL

The Contractor is responsible for all construction traffic control as specified by the most recent adopted edition of the Manual on Uniform Traffic Control Devices, which includes proper advanced warning signage, flaggers, shadow vehicles, etc. Painted Pavement Marking application will be performed under traffic.

#### J. PROPOSAL/PROJECT GUARANTEE

As evidence of good faith in submitting this proposal, enclosed herewith is a bid bond in the amount of five (5) percent of our bid, which, it is understood, shall be payment to ____________ County, not as a penalty, but in liquidation of damages to the County. The bond shall be forfeited if at any time subsequent to the opening of bids by ______________ County, Contractor fails or refuses to comply with any obligation or duty required of it in fulfillment of Contractor entering into the contract for which it is submitting this bid.

The bidder to whom the contract is awarded shall furnish within (10) ten days after the award a surety bond or bonds or certified check in a sum equal to the full amount of the contract. The form of the bonds and surety shall be acceptable to the ______________ County Board of Commissioners/Supervisors. Bonds/certified check for bid and performance bonds will be returned to bidder after satisfactory completion of project.

##### K. BID ITEMS

##### The bid item “Centerline” shall include the application of yellow paint and glass beads on the centerline of the road, which includes skip lines and no passing zones. Centerline shall be paid for at the unit price per mile actually painted.

##### The bid item “Edgeline” shall include the application of white paint and glass beads on both outside edges of pavement. Edgeline shall be paid for at the unit price per mile actually painted.

All materials, equipment, labor, and incidentals necessary to complete the work that is not paid for directly, shall be considered subsidiary to items for which payment is made.

##### L. INSURANCE REQUIREMENTS

The contractor shall not begin work under this Contract until it has obtained all insurance coverages required under this section and such insurance has been approved by the County.  The following insurance coverages shall be kept in force during the life of the Agreement and shall be primary with respect to any insurance or self-insurance programs covering the County, its commissioners/supervisors, officials, agents, representatives, and employees.

A.	Workers Compensation and Employers Liability Insurance

The minimum acceptable limits shall be the statutory limits as required by the State of Nebraska for Coverage A, Workers Compensation and $500,000 each accident for Coverage B, Employers Liability.

B.	Commercial General Liability Insurance

Coverage shall include liability coverage addressing premises and operations, contractual, independent contractors, and products/completed operations.  The coverage must protect against claims for damages resulting from bodily injury, including death, personal injury, and property damage.

The minimum acceptable limits of liability shall be $1,000,000 each occurrence.  If the coverage contains a general aggregate, such limit shall not be less than $2,000,000.  The products/completed operations limit shall not be less than $2,000,000.  If written on a claims made form, the products/completed operations coverage is to be maintained for two years after final payment.

The County is to be named as an additional insured on the insurance coverage required under this section.

C.	Automobile Liability Insurance

Coverage shall include liability coverage addressing claims for damages resulting from bodily injury, including death and property damage, which may arise from the operations of any owned, hired or non-owned automobile.  The minimum acceptable limit of liability shall be $1,000,000 Combined Single Limit for each accident.

The County is to be named as an additional insured on the insurance coverage required under this section.

D.	Certificate of Insurance

The Contractor shall furnish the County with a certificate(s) of insurance evidencing the coverages required in this section.  Such certificate(s)shall specifically state that the insurance company or companies underwriting these insurance coverages shall give the County at least thirty (30) days written notice in the event of cancellation of, or material change in, any of the coverages.  If the certificate(s) is shown to expire prior to completion of all the terms of this Agreement, the Contractor shall furnish a certificate(s) of insurance evidencing renewal of its coverage to the County.

The Contractor shall require each and every subcontractor performing work under this Contract to maintain the same coverages required of the Contractor in this section, and upon the request by the County, shall furnish the County with a certificate(s) of insurance evidencing the Subcontractor’s insurance coverages required in this section.

M. INDEMNIFICATION-HOLD HARMLESS

The contractor agrees to indemnify and hold harmless, protect and defend _______ County and its elected and appointed officials, employees, agents, and representatives against any and all claims, demands, suits, actions, payments, and judgments, including any and all costs and expenses connected therewith, legal cost or otherwise, for any damages which may be asserted, claimed, or recovered against or from _______ County or its insurers, because of personal injury, including bodily injury or death, or on account of property damage, including loss of use thereof, sustained by any person or persons which arises out of, is in any way connected with, or results from any and all work or activity associated with the services provided under this agreement unless such damages are the direct and sole result of _______County’s negligence.

COMPANY _____________________________

REPRESENTATIVE ______________________

DATE __________________________________

A site showing is required and will be set up by calling ___________, _____________________ County Highway Superintendent, XXX-XXX-XXXX between the hours of ___a.m and ___ p.m. Monday thru Friday.

_______________________ COUNTY RESERVES THE RIGHT TO REJECT ANY OR ALL BIDS AND TO WAIVE ANY INFORMALITIES OR TECHNICALITIES IN BIDS.

Painted Pavement Marking Project Location Map

_______________________ COUNTY

PAINTED PAVEMENT MARKING BID SHEET

In compliance with the Request for Painted Pavement Marking Bid and subject to all conditions thereof, the undersigned, having carefully read the specifications and familiarized himself with the conditions required to perform the proposed work, hereby offers and agrees, if this Quote be accepted within ten (10) days, to furnish all equipment and labor necessary to apply centerline striping, including no passing zone striping, and edge line striping to various roads in ____________ County, Nebraska at the prices set forth below and conforming in every respect to the specifications and all contract documents.

| ESTIMATED LENGTHS | ITEM | UNIT PRICE (PER MILE) DOLLARS CENTS | TOTAL PRICE DOLLARS CENTS |
| --- | --- | --- | --- |
| 1. ____ miles +/- | Centerline |  |  |
| 2. ____ miles +/- | Edgeline |  |  |

TOTAL QUOTE FOR PROJECT			$_________________________

APPROXIMATE START DATE			__________________________

APPROXIMATE COMPLETION DATE		__________________________

All work will be completed on or before __________________, 20___, weather permitting, unless other arrangements are agreed to by Contractor and Highway Department.

No proposal shall be considered binding upon ____________ County until the execution of the contract by both parties thereto.

_______________________ COUNTY RESERVES THE RIGHT TO REJECT ANY OR ALL BIDS AND WAIVE ANY INFORMALITIES OR TECHNICALITIES IN BIDS.

This proposal submitted this _____ day of ______, 20____.

_______________________________	__________________________________________________

Signature					Printed Name & Title

___________________________________________________________________________________

Address									Phone Number

State if an individual, partnership, or corporation:____________________________________________

If a partnership, give names and addresses of all partners._____________________________________

___________________________________________________________________________________

If a corporation, give state in which incorporated: ___________________________________________

PUBLIC NOTICE

PAINTED PAVEMENT MARKING CONTRACTORS

Sealed Bids, clearly marked "PAINTED PAVEMENT MARKING" will be received at the office of the _______________________ County Clerk, _______________________ County Courthouse, ________,  Nebraska, XXXXX, until ____ A.M. on _________, 20____, for approximately ______ miles of painted pavement marking.  Bids will be publicly opened and read at that time in the _______________________ County Board of Commissioners/Supervisors room during their regularly scheduled meeting.

For Specifications and Bid Documents, please contact the _______________________ County Highway Superintendent's office at________________.

_______________________ County reserves the right to reject any or all bids and to waive any informalities or technicalities in the bids.

Submitted

_______________________ County Highway Superintendent

__________________

---------------------------------------------------------------------------------------------------------------------

Notes to Publisher (not to be published)

- Publish at least once a week for three consecutive weeks prior to the week of _________, (include appropriate month, day, year)

  - First publishing shall occur at least 21 days prior to _____________. (include appropriate month, day, year)

  - First anticipated publishing is ___________ (month, day, year)

Provide two Proofs of Publication with Notary Public stamp and bill to:

________________ County Road Department

__________________

__________________

Sample “NOTICE TO PROCEED”

PAINTED PAVEMENT MARKING CONTRACTOR

NOTICE TO PROCEED

To:	________________				Date:		_______________

________________				Project: 	_______________

________________					   	_______________

You are hereby notified to commence work in accordance with the agreement/contract dated ______________, 20___, on or before _____________, 20____ and you are to complete the work within _______ consecutive calendar days thereafter. The date of completion of all work is therefore _____________, 20___.

__________________________________

________ County Highway Superintendent

__________________________________

Chairman, Board of Commissioners/Supervisors

ACCEPTANCE OF NOTICE

Receipt of the above NOTICE TO PROCEED is hereby acknowledged by ________________________, this the ____ day of ___________, 20____.

By __________________________

Title _________________________

____________________ COUNTY

PAINTED PAVEMENT MARKING BID COMPARISON SHEET

BID OPENING, ______, 20___   _____ a.m.

_____________________________________________________________________________

BID PER MILE		      TOTAL PROJECT BID

Centerline   	Edgeline

_____________________________________________________________________________

Straight Line Striping

423 Ponderosa Drive

Grand Island, NE

68803

308-384-4638

_____________________________________________________________________________

Contractor Services, Inc.

1320 East 8th Street

North Platte, NE

69101

308-221-2372

_____________________________________________________________________________

Traffic Safety Services

1900 Northern Plains Dr.

Bismark, North Dakota

58504

701-258-4770

_____________________________________________________________________________

Other

_____________________________________________________________________________

Other

____________________________________________________________________________________________________________